## Slide 1: Agenda
Basics of powder dosing
Gain-in-Weight technique
Example of setting up a GIW system
Troubleshooting for GIW inaccuracy
Lost-in-Weight technique
Example of setting up a LIW system
Troubleshooting for LIW inaccuracy

## Slide 2: BASIC OF DOSING: Dosing process unit
To accurately measure materials input and transport these materials into the next process
Can be a big group of machines or just a few instruments
Control key to successful product industrialization.

## Slide 3: BASIC OF DOSING: Powder dosing strategy
Basic of any dosing strategy: measure the amount to be included in the recipe, and how to put it in.
  For easy visualization, think of making your morning tea: you need to measure 2 teaspoons of sugar, and using the spoon, one by one, put those sugar into your cup of tea.
Common industrial set up will include:
  Material storage ( ie: A powder silo)
  Dosing unit input mechanism (ie: valve, star valve, screw feeder, vibrating belt)
  Scale (ie: a hopper with loadcell)
  Dosing unit output mechanism (ie: valve, star valve, screw feeder, vibrating belt)

## Slide 4: BASIC OF DOSING: Powder dosing strategy
For process system, there are 2 modes of production: continuous and batch.
To suit these modes of production, for powder handling, we need 2 methods: Gain-in-weight and loss-in-weight
  For gas/liquid handling, we have flow totalizer and flow rate as equivalent.

## Slide 5: Gain-in-weight Technique
Technique suitable for BATCH process
The required input parameter is WEIGHT PER BATCH (Quantity per batch)
The principle steps:
  Put material into a scale, bit by bit
  Use the scale to measure the amount of material GAINED
  When the material GAINED reach the desired weight (SET POINT), release the material to the next process.
  Repeat

## Slide 6: Gain-in-weight Technique
This technique is straight forward, and performance of dosing only depends on 2 factors:
  Scale Accuracy and Repeatability
  How well the dosing unit reach the SET POINT
Common problems:
  Scale linearity and scale calibration (ie: 100.5kg instead of the required 100kg)
  Overdosing due to dosing input mechanism dead time (ie: scale reached set point, but screw feeder need 1-2 second to fully stop dosing)
  Dosing accuracy vs speed (higher dosing accuracy needs longer time)

## Slide 7: Example: Setting up a GIW System
While powder dosing set up are more or less simple, we will start with a simple PFD (process flow diagram) of a GIW dosing unit and a BATCH Mixer
GIW-DOSING
BATCH MIXER

## Slide 8: Example: Setting up a GIW system
Let’s furnish with more of system details for GIW-Dosing unit
SCALE HOPPER
MATERIAL STORAGE SILO
OUTPUT
VALVE
BATCH
MIXER
GIW DOSING UNIT
QUANTITY PER BATCH
INPUT
SCREW
FEEDER

## Slide 9
SCALE HOPPER
MATERIAL STORAGE SILO
OUTPUT
VALVE
BATCH
MIXER
GIW DOSING UNIT
INPUT
SCREWFEEDER
GIW
CONTROLLER
QUANTITY PER BATCH
To adjust the speed of screw feeder, a Variable Speed Driver (or Variable Frequency Driver/Inverter) is installed. A slower speed means higher accuracy might be achieved.
After the quantity in scale hopper is equal to Quantity per batch, Input Screw feeder stop, Output Valve Open to let all the material in Scale hopper to go to Batch Mixer
VSD

## Slide 10: Basic control scheme for GIW
BATCH START
TARE SCALE HOPPER, WEIGHT = 0
RUN INPUT
SCREW FEEDER @100%
GET SCALE HOPPER READING W1
IF (W1 > Wbatch – 8kg)
RUN INPUT
SCREW FEEDER
@5%
GET SCALE HOPPER READING W1
IF (W1 > Wbatch)
STOP SCREW FEEDER
@0%
OPEN OUTPUT VALVE UNTIL W1 = 0
BATCH END
GET SCALE HOPPER READING W1
NO
NO
YES
YES

## Slide 11: Troubleshooting in GIW dosing accuracy
Check scale calibration report for linearity and accuracy
Check input dosing mechanism for any deviation (leak, overrun, momentum etc)
Check if there are any interference to input dosing mechanism and to scale during scale and input dosing

## Slide 12: Lost-in-Weight technique (LIW)
Technique suitable for CONTINUOUS PROCESS
The required input parameter is WEIGHT OVER TIME (Feed rate set point)
The principle steps:
  Put material into a scale
  Start the dosing output mechanism for a period of time
  Measure the value of material LOST from the scale
  Calculate the weight lost over time (Lost in weight) and compare it to the SET POINT
  Calculate and adjust the speed of dosing output mechanism to reach SET POINT
  Repeat to step 2

## Slide 13: Lost-in-Weight Technique (LIW)
In comparison to Gain-in-Weight, Lost-in-Weight requires more calculation, and there are more ways this technique can go wrong
More often, issues with Lost-in-Weight is reported only after compilation of materials used in process over a long period of time, thus, making this harder to troubleshoot and find the root cause of inaccuracy.

## Slide 14: Example: Setting up a LIW system
While powder dosing set up are more or less simple, we will start with a simple PFD (process flow diagram) of a LIW dosing unit and a continuous Mixer
LIW-DOSING
CONTINUOUS MIXER

## Slide 15: Example: Setting up a LIW system
Let’s furnish with more of system details for LIW-Dosing unit
SCALE HOPPER
MATERIAL STORAGE SILO
INPUT VALVE
CONTINUOUS MIXER
OUTPUT SCREWFEEDER
LIW DOSING UNIT
FEEDRATE SETPOINT

## Slide 16: Example: Setting up a LIW system
The SILO and valve are used to keep the size of the Scale hopper manageable. If the scale hopper is too big, it will require a high-capacity loadcell, thus, more errors. However, this will introduce the process of refilling scale hopper.
The scale hopper is the main measuring point of weight. A good and frequent calibration and linearity check is required to maintain high accuracy of the system
A screw feeder is used to maintain a continuous feed rate to the continuous mixer
SCALE HOPPER
MATERIAL STORAGE SILO
INPUT VALVE
CONTINUOUS MIXER
OUTPUT SCREW FEEDER
LIW DOSING UNIT
FEEDRATE SETPOINT

## Slide 17
SCALE HOPPER
MATERIAL STORAGE SILO
VSD
CONTINUOUS MIXER
LIW DOSING UNIT
FEEDRATE SETPOINT
OUTPUT
SCREW FEEDER
ENCODER
INPUT
VALVE
LIW CONTROLLER
To adjust the speed of screw feeder (thus, feed rate), a Variable Speed Driver – VSD (or Variable Frequency Driver/Inverter) is installed
To make sure the speed of the screw feeder is well controlled, speed reading is required, and done via an installed encoder on the motor
Feed rate set point, encoder and scale are all processed by a LIW Controller to output a desired frequency to the VSD  Output screw feeder  FEED RATE.

## Slide 18: Basic control scheme of LIW: DOSING
Get reading from scale W1 kg
Output Screw feeder run at speed F1 Hz in T second
Get Encoder
cycle count R1
Get reading from Scale W2 kg
Calculate Output Screw feeder speed (R1/T)
Calculate Feed rate
(W1-W2)/T
Calculate relationship between OutputScrew feeder speed and Feed rate
Calculate and set new frequency F1 to match feed rate and feed rate set point
START
DOSING SEQUENCE

## Slide 19: Basic control scheme of LIW: REFILLING
Get scale reading W
If W < Wmin
Open INPUT Valve
If W > Wmax
Close INPUT Valve
Get scale reading W
Keep Screw feeder at previous frequency
(REFILL MODE)
Restart Calculate Screw Feeder Frequency
(PRODUCTION MODE)
NO
NO
YES
YES
Start
REFILLING

## Slide 20: Extra features in LIW
Some LIW Controller might include extra features:
  Encoder cycle / weight (Pulse per unit) profile. This number, if divide by time, will be screw feeder speed / feed rate. This PPU will be used to stabilized uncertainty / vibration noise introduce in scale hopper by refilling / screw feeder vibration / other source of vibration
  PPU profile at each weight load in scale hopper
  PID control to match current feed rate with feed rate setpoint
  Safety function when the level is too low / too high
  Noise cancellation
  Database of previous profiles
All the extra features will help to stabilize system as much as possible

## Slide 21: Troubleshooting for LIW Dosing error
Check calibration report for accuracy and linearity
  There are cases of wrong system installation, thus introduced scale nonlinearity
Check the function of VSD and encoder
  If VSD is stable, the frequency output will be fairly stable
  Use a oscilloscope to health check the encoder. If it is good, the frequency output will be stable
Check the parameter setting of LIW controller
  PID
  Encoder setting, conversion
  VSD communication
  Dosing calculation / result
  Overall condition of LIW controller
Monitor the dosing trends
  Identify sources of noise, and eliminate if possible.

## Slide 22: THANK YOU FOR YOUR ATTENTION